## Slide 1: AMS at ATLAS May 16, 2014
Richard Pardo

## Slide 2: Outline
Features of ATLAS for AMS
  ‘High’ beam energy
  Sophisticated detector systems allow unique ‘Z’ ID into A~150
    FMA and associated detector system
    Enge Spectrograph and associate detector system
  Stable operation and sophisticated control
    Work underway to approach flexibility of dedicated AMS facility.
    Development of laser ablation system to improve cross-talk
Current AMS activity focus:
  146Sm
    Astrophysical chronometer (T½ = 68 M years)
    Nuclear Physics data
      (α, γ) σ
      (n, γ ) σ
  Actinide Integral neutron capture cross-sections for reactor studies and design (MANTRA)

## Slide 3: ATLAS AMS Typical Configuration
PII LINAC
Booster Linac
Split-pole Spectrograph
Fragment Mass Analyzer
ECR-II Ion Source

## Slide 4: ATLAS Features Important for AMS
ATLAS is the only AMS facility where mid-heavy nuclides (A~100-150) can be uniquely identified
  Requires ensuring high-energy reliability of ATLAS (E > 8-9 MeV/u)
    Reliable, rapid switching between different M/q species
  AMS measurements require stability
    Recent ATLAS upgrades are contributing to this
      RFQ repeatability and reliability is excellent
      New cryostat resonators operate in new ‘driven’ mode
        VCX PIN diodes eliminated

## Slide 5: MANTRA: An Integral (n, γ) Cross-Section Measurement
Objective of the experiment:
Infer effective neutron capture cross-sections of most actinides of interest for reactor physics in fast and epithermal spectra (a few fission products are also considered)
Consistency of the fast and epithermal data (i.e. same samples, same fabrication protocols, same PIE protocols, same experimentalists, etc…)
Uses multi-collector ICM-MS and AMS at ATLAS to measure nuclei produced during ~60 day neutron irradiations in the ATR at INL
Approximately 30 unique samples will need to be measured. Desired precision is better than 5%.

## Slide 6: Three filters provide different neutron energy regimes
Effect of neutron filters on the neutron spectrum in the samples
Irradiation is performed at the ATR at Idaho National Laboratory

## Slide 7: MANTRA: An Integral (n, γ) Cross-Section Measurement
Objective of the experiment:
Three neutron spectra
Seven actinide ‘mother’ materials.
  235U, 238U, 237Np, 242Pu, 244Pu, 243Am, 248Cm
  Plus the original un-irradiated material
Approximately 28 unique samples will need to be measured.
Desired precision is better than 5%.
Significantly more complex and precise than most AMS experiments at ATLAS.
  Drives the need for significant accelerator and ion source improvements.

## Slide 8: Facility Improvements Required for MANTRA
ATLAS Improvements required for achieving MANTRA Goals
  Laser ablation of material into the source
    Goal is reduced cross-talk between samples
    Higher total efficiency
  Multi-sample changer
    Holds up to 20 samples
    Allows rapid cycling between samples
  Control system programmable to allow rapid configuration changes
    All dipoles set by gauss
    Magnetic quadrupoles set using a specific pattern to reduce hysteresis effects
    Multiple (M/q) configuration stored
      Rapid switching between configuration automatically by master clock
      Normalization by beam current at source or base material measurement at detector
        Precise attenuation with non-resonant beam sweeper.

## Slide 9: Laser Ablation into ECR Ion Source
Multisample Changer
Laser
Beam Out to Linac
Laser
High voltage platform
Optical elements
Bending magnet
Focusing lens
ECR
Laser placed off platform and focused through ECR with 4m lens
Laser reliability and performance still not as good as desired.
5 mJ/pulse, 1064 nm,
10 picosecond pulses
0.5 mm diameter beam spot
Cos θ angular distribution
3mm

## Slide 10: Multi-Sample Changer for Source
Multi-sample changer at ion source
20 samples on retractable rods
Allows rapid switching between samples
Positions samples slightly off-axis of source
First tests with changer have gone extremely well.

## Slide 11: AMS Demands Benefit ATLAS Operation
The needs of the AMS program have driven significant improvements at ATLAS
  Laser ablation of material into the source and Multi-sample changer
    Successful development of laser ablation will benefit ATLAS Operation
      Less source contamination
      Ability to rapidly switch beams
      Less start-up time
  Control system improvements speed ATLAS beam changes.
    All dipoles set by gauss
    Magnetic quadrupoles set using a specific pattern to reduce hysteresis effects
    Multiple (M/q) configuration stored
      Rapid switching between configuration automatically by master clock
      Normalization by beam current at source or base material measurement at detector
        Precise attenuation with non-resonant beam sweeper.
  Push to go to an M/q of 8 for the heaviest beams
    Important for actinide AMS
    Higher beam currents for other programs.
Runs for actual irradiation measurements should be ready to begin in August.

## Slide 12: Summary
Use of ATLAS for Accelerator Mass Spectroscopy provides unique capabilities, especially for mid-mass regime
Actinide AMS with ATLAS makes use of in-place equipment and ion source expertise

## Slide 13
MR-TOF for High Sensitivity Mass Spectroscopy

## Slide 14: MR-TOF for Mass Spectroscopy