## Slide 1: Neutron Spectroscopy with Ion Traps for Astrophysics
Nicholas Scielzo
Experimental Nuclear Physics Group
Astrophysics Working Group
ATLAS/CARIBU User’s Meeting 2014
May 15, 2014

## Slide 2: Rapid neutron-capture process nucleosynthesis
Peter Moller, LANL
Neutrons added through successive rapid (n,g) reactions
Very neutron-rich isotopes are produced
At some point (n,g) is balanced by (g,n) until b decay occurs
At high enough masses, fission breaks up nuclei
stability
r-process path
Final abundances determined from astrophysical conditions (n density, temp.) and nuclear properties
Sn (masses)
β-decay half-lives
(n,g) cross sections
fission properties
b-delayed neutron emission (Pn)
r process responsible for production of ~half heavy elements in very neutron-rich HED environments
Abundance pattern extracted from Solar System and certain metal-poor stars in halo of galaxy

## Slide 3: b-delayed neutron impact on understanding r-process nucleosynthesis
r process path
(very neutron rich!)
stable nuclei
Pn~40%?
n
K.-L. Kratz et al., Astron. Astrophys. 125, 381 (1983)
?
At end of r process, exotic short-lived nuclei b decay back to stability
During multiple decays, b-delayed neutron emission can change mass of nuclei
Pn branching ratios influence final mass distribution
Also provide additional neutrons during freeze out

## Slide 4: New approach to neutron spectroscopy… without detecting neutrons
b
n
Neutron emission
n
n (1 MeV): ~10 keV recoil
Identify neutron emission from larger nuclear recoil.
Avoid neutron detection.
Perform delayed-neutron spectroscopy by detecting recoiling daughter ions emerging from an ion trap
b (1 MeV): ~0.01 keV recoil
Need: Access to low-energy nuclear recoil
Way to precisely measure recoil energies
Efficient for any isotope with t1/2 > 50 ms
Use ion trap… measure recoil energy from TOF

## Slide 5: The Beta-decay Paul Trap
Works for any element
Confine up to 105-106 ions at once
Hold for >200 sec
Accessible half-life > 50 ms
Confine in ~1-mm3 volume

## Slide 6: Outfit the Beta-decay Paul Trap with different radiation detectors
137I  137Xe* + b- + n
136Xe + n
n
136Xe++
137I+
MCP
Trap electrodes
Principles
Trap bn precursors as ions
Cool by He gas to ~1-mm3 volume
Ions decay from rest at trap center
Trigger on β’s using plastic
Measure recoil time of flight (TOF) to MCP
  β (+g) gives lower energy recoil (< 170 eV)
  β+n gives higher energy recoil (up to 14 keV)
  Advantages
  Measurement of both Pn and En
  High efficiency and good En resolution
  Insensitive to background g’s & n’s
  Near-Gaussian En detector response
  Efficiency nearly independent of En
  Many checks of systematic effects
  Challenges
  Trapping field perturbs ion trajectory
  Ion cloud size
HPGe
HPGe
Plastic
ΔE-E
ν
β

## Slide 7: Data collected with 137I+ beam of 30 ions/sec from an offline 1-mCi 252Cf source
137I b decay in the trap (Pn=7%)
137Xe ions following b decay
Counts/6.5 ns
Time of flight (ms)
Time of flight (ms)
136Xe ions following neutron emission
Counts/13 ns
b-delayed neutron energy spectrum

## Slide 8: Upgrades  higher statistics and reduced systematic effects
Increase b efficiency + spectroscopy
2× DE-E plastic scintillators subtend ~10%
Detector in rough vacuum separated from UHV by 10-mm window
Increase recoil-ion efficiency and improve measurement of En
2× 50x50-mm2 MCP subtend ~10%
Position sensitivity (<1 mm) allows path length reconstruction
Different b-ion angle combos
Reduce En threshold  better separation of b and bn recoils
Electrodes closer to center
RF applied only to ends of electrodes
MCP
Trap electrodes
HPGe
HPGe
Plastic
ΔE-E
MCP
Plastic
ΔE-E
11mm
Vrf = 85 V

## Slide 9: BPT moved down to the CARIBU Low-Energy Experimental Hall –Nov.-Dec. 2013 Measurement Campaign
137,138,140I
144,145Cs
134,135,136Sb
101 -102
~101
102 -103
Ions/sec at BPT

## Slide 10: Analysis of this data is underway…
137I
138I
140I
134Sb
135Sb
144Cs
145Cs
136Sb
calibration

## Slide 11: Design for a dedicated trap
Compact rod structure for electrodes  minimize perturbation on recoil ions
Larger detector array (x4 increase in coincident eff. vs. 2013)  4 MCPs, 8 ΔE-E plastic scintillators, 4 HPGe clovers
Couple to a low-energy CARIBU beamline
A. Levand (ANL)

## Slide 12: Existing/future capabilities
 | Proof-of-Principle (2011) | Upgraded trap (2012-2013) | New ion trap (2015)
Trap radius | 17 mm | 11 mm | 7 mm
Vrf | 200 V | 100 V | ~30 V
En resolution | 10-20% | 5-10% | 5-10%
En threshold | 200 keV | 100 keV | ~50 keV
b threshold | 150 keV | 50 keV | 25 keV
b-ion coinc. eff. | 0.04% | 0.7% | 3%
Sensitivity | ~20 ions/s | ~1 ion/sec | ~0.1 ion/s

## Slide 13: Ultimate reach of ion-trap approach is ~0.1 ion/sec (any isotope shown in color)
In addition to beam intensity, to reach most neutron-rich isotopes also need suppression of isobars by >102
Can collect high-quality data on isotopes near/on the r process path

## Slide 14: Ion Trap Collaborators
N.D. Scielzo, A. Czeszumska, E.B. Norman, S. Padgett, R.M. Yee,
G. Savard, S. Caldwell, J.A. Clark, A.F. Levand, A. Perez Galvan, M. Burkey
F. Buchinger, R. Orford
R. Segel
K.S. Sharma, G. Morgan
Graduate Students
Postdoctoral Researchers
A. Aprahamian, S. Marley, N. Paul, S. Strauss, K. Siegl
C.J. Chiara, J. Harker