## Slide 1: Potential Upgrades to the LENA Detector System
David Little

## Slide 2: Laboratory for Experimental Nuclear Astrophysics (LENA)

## Slide 3: Laboratory for Experimental Nuclear Astrophysics (LENA)

## Slide 4: Present LENA HPGe Detector
Thoroughly characterized
P-type coaxial HPGe detector
91.6 mm deep and 89 mm in diameter
Dead layer of 1.5 mm
Surrounded by 16 NaI(Tl) scintillators
S. Carson, et al., Nucl. Instrum. Methods A
NaI annulus
Beam pipe
HPGe detector

## Slide 5: My Reaction: 25Mg(p,γ)26Al
Astrophysically relevant
Specifically want to examine the 92 keV resonance
  Important for massive stars (temps between 40-90 MK)
Very weak resonance strength (2.9 x10-10 eV)
Nothing else is known
Likely to fall below our present detection limits
Iliadis et al. 2011

## Slide 6: WHAT DO WE DO?

## Slide 7: Solutions
Beam pulsing the ECR ion source should allow us to significantly reduce environmental background
Upgrading the detector design could provide a much higher γ-ray detection efficiency
Photo courtesy of Andrew Cooper

## Slide 8: Clover
Four P-type coaxial HPGe crystals
70 mm x 70 mm x 70 mm per crystal
Quoted dead layer of .5 mm
γ-ray add-back feature
Roughly $600,000

## Slide 9: Cluster Array
Seven P-type coaxial HPGe crystals
78mm in length
Cylinder morphs into hexagonal face
70mm diameter cylinder
61mm flat to flat hexagons
Quoted dead layer of .5mm
Individual Al casing for each crystal
γ-ray add-back capability
Around $1,000,000

## Slide 10: Efficiencies with Respect to LENA
Clover and Cluster have peak efficiencies of about 2 and 2.4 times LENA, respectively
Plots courtesy of A.E. Champagne
Notes: Graph of ratios

## Slide 11: The Next Step
Must simulate background along with signal
Included 40K, 232Th chain, 238U chain, m+ and m- and fraction fit based on lab background spectrum
Created hypothetical decay for 92 keV resonance in 25Mg(p,γ)26Al
  60% branch to ground and 40% branch to isomer (first excited state)
Calculated expected 26Al yield assuming an infinitely thick target, 2 mA of beam and 3 weeks of run time
Should see around 16,000 reactions
Combined this all into a single simulation
Applied γ-γ coincidence gate to reduce background
where
(cm2)

## Slide 12: The Clover Falls Short
Clover

## Slide 13: The Clover Falls Short
LENA

## Slide 14: What Now?
The clover detector doesn’t appear to provide any advantage for detecting the 25Mg(p,γ)26Al decay signal
  Has to do with how the energy gates are set and the γ-ray energies produced by the environmental background and the reaction
Simulating a thicker lead shield around the detector showed a significant increase in low energy background due to Compton scattered events
The only option left is to pulse the ECR ion beam

## Slide 15: Beam Pulsing
Simulated present detector setup assuming 5 mA of beam pulsed at a 20% duty cycle for 6.2 days
Compared with 2 mA of DC beam
Significant signal improvement can be seen with pulsed beam

## Slide 16: Future Plans
Set up a system for tuning on pulsed beam
Measure 25Mg(p,γ)26Al with pulsed ECR beam
Find sweet spot for Pb passive shielding for clover
Write and submit proposal for clover detector
Learn things

## Slide 17: Thanks
Art Champagne, Christian Iliadis and Richard Longland
Sean Hunt, Andrew Cooper, Jack Dermigny and Lori Downen
The MAJORANA Demonstrator group at UNC
A special thanks to Reyco Henning and Chelsea Bartram for their assistance, as well as to the DOE for funding this research

## Slide 18: References
[1] C. Iliadis, Nuclear Physics of Stars, Wiley-VCH, Weinheim, 2007
[2] G.F. Knoll, Radiation Detection and Measurement, Wiley, New York, 1989
[3] S. Carson, et al., Nucl. Instrum. Methods A: 618 (2010) 190
[4] C. Howard, et al., Nucl. Instrum. Methods A: 729 (2013) 254
[5] S. Agostinelli, et al., Nucl. Instrum. Methods A: 506 (2003) 250

## Slide 19: Extra Slides

## Slide 20: The Whys and Hows
If 26Mg excess in CAIs is due to 26Al, it is possible for these inclusions to serve as chronometers for early solar system events
Isotopic ratios are measured to determine mass excesses of 26Mg and thus 26Al
MacPherson et al. 1995

## Slide 21: Confusion
26Al/27Al ratios measured from CAI inclusions in Allende meteorite (Lee et al. 1976)
Inclusions appeared to have formed from two separate reservoirs with ratios of 0 and 5x10-5
MacPherson et al. 1995

## Slide 22: The Gold Standard
In fact, it was a single reservoir but lower ratios are due to melting and recrystallization of the meteorite
5x10-5 is the gold standard corresponding to the initial isotopic ratio of Al injection into the presolar nebula
Assuming this initial value, the age of different CAIs can be determined
This ratio and the aging of CAIs can be very useful tools for unearthing the history of our solar system

## Slide 23: Evidence
Half-life of 7.17 x 105 years
Time scale for galactic evolution is roughly 1010 years
Short half-life provides a snapshot of the galaxy
Direct observation of 1809 keV γ-ray
26Mg excesses in presolar grains and CAIs
myriamtelus.files.wordpress.com
Falling Stars Inc.
NASA

## Slide 24: The Source
Big mystery!
Multiple possibilities for synthesis of 26Al
  Wolf-Rayet stars
  Supernovae
  AGB stars
  Classical novae
MacPherson et al. 1995

## Slide 25: My Focus
Focused primarily on the possibility of 26Al generation from Supernova nucleosynthesis
Explosive Carbon Neon burning in massive stars
Follows directly from Iliadis et al. 2011
Main difference is the analysis of Monte Carlo rate variation on the 26Al/27Al ratio

## Slide 26: Supernova Flux
Lots of things happen during supernovae

## Slide 27: Temperature-Density-Time Comparison
Temperature peaks at around 2.3 GK
26Al production stops at about 12.8 seconds
Iliadis et al. 2011

## Slide 28: Temperature-Density-Time Comparison
Density peaks at around 3.2x105 g/cm3
26Al production stops at about 12.8 seconds
Iliadis et al. 2011

## Slide 29: Mass Fraction Comparison
26Al jumps from about 3x10-6 to 1x10-4 during the explosion
27Al abundance is roughly unchanged
Iliadis et al. 2011

## Slide 30: Effect of Rate Variations on 26Al
26Al(n,p)26Mg

## Slide 31: Effect of Rate Variations on 27Al
27Al(α,p)30Si
30Si(p,α)27Al

## Slide 32: Effect of Rate Variations on 26Al/27Al
26Al(n,p)26Mg
27Al(α,p)30Si
30Si(p,α)27Al

## Slide 33: New Reactions of Interest
The effect of rate variations on the 26Al/27Al ratio has not been explicitly analyzed before
Important reactions established Iliadis et al. 2011 were 26Al(n,p)26Mg, 25Mg(α,n)28Si, 24Mg(n,γ)2Mg and 23Na(α,p)26Mg
New reactions of interest are 27Al(α,p)30Si and 30Si(p,α)27Al
Resonances for these reactions occur at much higher energies than we can measure at LENA

## Slide 34: Other Possibilities
Production of 26Al in massive Wolf-Rayet stars (25 solar mass red giants)
92 keV resonance for 25Mg(p,γ)26Al is an ideal measurement for LENA’s ECR ion source (80 – 200 keV energy range)
Photo courtesy of Andrew Cooper

## Slide 35: Efficiencies

## Slide 36: Final Test
Must simulate background together, along with 25Mg(p,γ)26Al in order to see if the reaction could be observed
Coincidence gating must be applied during analysis in order to mitigate background
However, enough simulations must be run such that the application of coincidence gating does not remove all background statistics
Effectively, about 6 trillion background simulations must be run in order to model 3 weeks worth of beam time

## Slide 37: How in the Heck?
New Longleaf computing cluster at UNC
Built for large amounts of parallel jobs each requiring a single compute host
Maximum of 1000 jobs at a time
Free!!!
Photo courtesy of wisegeek.com