## Slide 1: Modular Superconducting Quantum Computing
Srivatsan Chakram, Alex Ma, Yao Lu, Ravi Naik, Nelson Leung, Clai Owens, Brendan Saxberg, Nate Earnest, Abigail Shearrow, Jens Koch
David Schuster
Department of Physics and James Franck Institute, University of Chicago

## Slide 2: Schoelkopf’s law – Coherence 10x every 3 yrs!
Quantum Error Correction threshold?
Heavy fluxonium
(chicago)
On the threshold of error correction!
Reason to believe we can get to >1s!
2D transmon IBM

## Slide 3: Ignition!
Quantum Error correction is the equivalent of ignition
Where you get exponential gain with more fuel (qubits)

## Slide 4: Outline
A modular architecture for superconducting quantum computing
Multimode Circuit QED
Universal local operations
Deterministically transmitting quantum information

## Slide 5: Microwave photons in a superconducting box
If we take a single resonant mode of any of these boxes it looks like a harmonic oscillator
Many types of “boxes”

## Slide 6: Superconducting qubits (two level system)
Many flavors of qubit
Key element is the Josephson Junction
Anharmonic Oscillator
Charge
Transmon
Flux
Junction acts as non-linear inductor
Bottom two (or several) individually addressable

## Slide 7: A photonic modular architecture for SC qubits
Advantages:
10-100 qubits per module
10x fewer transmons, 10x less classical hardware
Fully connected: 2 hops between any pair of bits, M-bits in parallel
Compatible with hardware efficient error correction

## Slide 8: Modular Universal Quantum Logic
Single qubit gate (2 swaps)
Intra-module two qubit gate (4 swaps)
Inter-module two qubit gate (8 swaps)
Only two types of operations (rotation and swap)
Inter-module almost as fast as intra-module
Can run M instructions in parallel

## Slide 9: A network of two multimode-processors
2 chips each with:
1 Transmon control
1 Measurement channel
8 data qubit modes
1 communication link
Many photonic qubits
Multiplexed control
Universal Multimode Ops
Modular architecture
Notes: As was described in previous talks, we have a nice multimode CQED architecture with multiple photonic qubits over which we have multimplexed control using a single flux tunable transmon qubit. In this talk we describe how we perform multiplexed state characterization. This is necessary because we have I transmon, and therefore one measurement channel.
In this talk we will describe how we use our toolbox of single of and two-qubit operations

## Slide 10: How does an FM radio work?
Carrier Frequency
Modulation signal

## Slide 11: Stimulated Vacuum Rabi Oscillations

## Slide 12: Stimulated Vacuum Rabi Oscillations
Transmon State
Multimode State
We use a parametric drive to stimulate a vacuum Rabi Oscillation with any mode
Address many modes with just a single transmon and set of controls

## Slide 13: Randomized Benchmarking of light
swap
swap
Qubit
rotate
Qubit: >98%
Cavity mode
Fidelity: 90-97%

## Slide 14: Anatomy of a multimode gate
CZ

## Slide 15: Anatomy of a multimode gate
CZ
CNOT

## Slide 16: Anatomy of a multimode gate
Dispersive shift
Stimulated AC Stark shift
Qubit DC offset during Gate
Working to model, compensate these higher order terms

## Slide 17: Process tomography of multimode gates
CZ
Fidelity ~80% for gate
Random access quantum information processors. Nat. Comm. 8, 1904 (2017)

## Slide 18: Shuttling single photons
Readout
Multimode Memory
Communication
Everything is accessed with sideband swaps.
Communication looks just like memory!

## Slide 19: Low loss communication channel
T1: 550ns
T2*: 1us
Model as 3 modes in series
Comm – cable – Comm
Dark mode is protected against loss in cable!
T1 = 550ns

## Slide 20: Bi-directional photon transfer
Qubit 1
Qubit 2
1. Put single photon in sender
2. Swap into “dark” mode
3. Swap into receiver
Can speed things up by sending and receiving simultaneously.
Notes: we can simultaneously turn on both sideband pulses with equal amplitude, till the photon is maximally transferred from one side to another. This scheme has two advantages: one, the transfer time is shorter than two complete sideband pi pulses,

## Slide 21: Bidirectional photon transfer
eg
gg
ge
ee
ge
gg
eg
ee
2 to 1 fidelity: Peg0 ≈ 62 %
Loss mechanism:
  qubit and channel decay: Pgg0 ≈ 24%
  qubit dephasing: Pgg1+ Peg0 ≈ 14%
1 to 2 fidelity: Pge0 ≈ 61 %
Loss mechanism:
  qubit and channel decay: Pgg0 ≈ 24%
  qubit dephasing: Pgg1+ Peg0 ≈ 15%
Pgg1
Pgg1
Peg0
Pge0
Qubit 1
Qubit 2
Qubit 1
Qubit 2
Notes: Similarly, the dephasing of the sender qubit also leads to some population residue not transferred. Numerical simulation shows that the total qubit dephasing loss contributes to a 15% and a 14% infidelity in these two transfer processes.

## Slide 22: Bell state generation
Qubit 1
Qubit 2
Loss mechanism:
  qubit and channel decay: 0.1
  qubit dephasing: 0.1
Sending half the photon creates Bell state
Notes: From master equation simulation, we estimate that the qubit and channel decay loss, and qubit dephasing loss each accounts for half of the infidelity.

## Slide 23: Realizing higher Q - 3D modules
A box with no seams.
10-50 Modes
Engineered dispersion uniformly spaced (400MHz)

## Slide 24: Other exciting projects in the lab
cQED with electrons on helium
Protected qubits
PRX 6, 011031 (2016)
PRB 90, 094518 (2014)
Autonomous error correction
w/ E. Kapit
Rydberg
Optical/Microwave CQED
w/ Jon Simon
Searching for Dark Matter
w/ Aaron Chou, and others at FNAL

## Slide 25: The group

## Slide 26: Conclusions
Modular superconducting architecture with random access, reduced resources
Universal quantum logic within a module
Bi-directional coherent communication ~60% single photon fidelity
Remote Bell state generation ~80% Bell state fidelity
Higher Q 3D implementations soon
Superconducting Qubits can be used directly as sensors